## Slide 1: German Digital Signature Card and Office Identity Card and PKCS #15
Bruno Struif
GMD
German National Research Center for Information Technology
Darmstadt

## Slide 2: General Configuration
Card
Terminal
PC
ICC1
ICC2
ICC3
Application
PKCS#11
Interface
Different cards
with PKCS#15
Smartcards
providing the
same service,
but possibly
in a different way.
- If a PC application knows to deal with a card application, no directory files are necessary
- If a PC application does not know how to deal with a card application, it needs information

## Slide 3: Is PKCS#15 powerful enough?
Some challenges:
- cards may have a hash function or not
- cards may support different signature algorithms
- cards may support a different set of Digital Signature Input formats
- a card may be configurated in such a way that it allows - either after PIN presentation an unlimited number of DS - or requires PIN presentation before each DS
- a card may support ETSI PIN management commands instead of ISO-commands - a card may support a proprietary command for a certain security service

## Slide 4: Card File Structure (1)
MF
EF(DIR)
DF(PKCS#15)
Other
DFs/EFs...

## Slide 5: Card File Structure (2)
DF(PKCS#15)
EF(ODF)
EF(PrKDF)
EF(CDF)
EF(AODF)
EF(TokenInfo)
EF(ODF) - Object Directoty File - points to
- EF (PrKDFs) - Private Key Directory Files
- EF (PuKDFs) - Public Key Directory Files
- EF (SKDFs) - Secret Key Directory Files
- EF (CDFs) - Certificate Directory Files
- EF (DODFs) - Data Object Directory Files

## Slide 6: Cross-References
EF(PrKDF)
EF(AODF)
EF(CDF)
EF(DODF)
EF(ODF)
PuKDF pointer
PrKDF pointer
CDF pointer
AODF pointer
DODF pointer
EF(PuKDF)

## Slide 7: Card File Structure (3)
MF
EF(DIR)
Other
DFs/EFs...
DF(PKCS#15)
EF(ODF)
EF(PrKDF)
EF(CDF)
EF(AODF)
EF(TokenInfo)
Real objects

## Slide 8: Card File Structure (4)
MF
EF(DIR)
DF1
DF(PKCS#15)
EF(ODF)
EF(PrKDF)
EF(CDF)
EF(AODF)
EF(TokenInfo)
DF2
Real objects
Real objects

## Slide 9: Card File Structure (5)
MF
EF(DIR)
DF(PKCS#15)
DF2
DF1
EF(ODF)
EF(TokenInfo)
EF(PrKDF)
EF(CDF)
EF(AODF)
EF(PrKDF)
EF(CDF)
EF(AODF)

## Slide 10: User Authentication
PKCS15 describes PINs and passwords, but no biometric user authentication
The German Digital Signature law allows biometric user authentication
It is technically already feasible to implement biometric feature matching algorithms in cards
ISO/IEC will add an amendment to 7816-4 with respect to biometric user authentication

## Slide 11: VERIFY Command
- If a digital signature is made on a private PC, then the PIN is presented as plain value
- If a digital signature is made on a public customer service terminal, then the PIN shall be presented as cryptogram followed by a cryptographic checksum

## Slide 12: Proposal for integration of bio objects (1)
PKCS15Authentication ::= CHOICE { pin PKCS15AuthenticationObject { PKCSPinAttributes },
bio PKCS15AuthenticationObject { PKCSBioAttributes },
}
PKCS15BioAttributes ::= SEQUENCE { bioFlags PKCS15BioFlags, bioSubject PKCS15BioSubject, bioType PKCS15BioType, bioReference [0] PKCSReference DEFAULT 0, lastBioChange GeneralizedTime OPTIONAL, path PKCS15Path OPTIONAL, ... -- For future extensions }

## Slide 13: Proposal for integration of bio objects (2)
PKCS15BioFlags ::= BIT STRING { reserved (0), local (1), change-disabled (2), unblock-disabled (3), initialized (4), reserved (5), reserved (6), reserved (7), disable-allowed (8), authentic (9), enciphered (10), }

## Slide 14: Proposal for integration of bio objects (3)
PKCSBioSubject ::= CHOICE { fingerPrint [0] FingerPrint, voicePrint [1] VoicePrint, irisPrint [2] IrisPrint, facePrint [3] FacePrint, retinaPrint [4] RetinaPrint, handGeometry [5] HandGeometry, writeDynamics [6] WriteDynamics, keystrokeDynamics [7] KeystrokeDynamics, lipDynamics [8] LipDynamics, ... -- For future extensions }

## Slide 15: Proposal for integration of bio objects (4)
FingerPrint ::= SEQUENCE { handID HandID, fingerID FingerID } HandID ::= ENUMERATED {righthand (0), lefthand (1) } FingerID ::= ENUMRATED { thumb(0), pointer finger (1), middle finger (2), ring finger (3), little finger (4) }

## Slide 16: Access to objects
Public Object
Private Object
„Entity Object“
Access is free
Authentication
Object has to be
presented
(PIN, password,
biometrics)
Authentication
procedure
has to be performed

## Slide 17: Management of Access Rights
Elementary File
Security
Attributes
File
Content
Example:
AM = Read
SC = EXT AUTH (asym) with
CHA = ´x.01´ or ´x.02´ and User AUTH
AM = Update
SC = EXT AUTH (asym) with
CHA = ´x.01´ and SM
X = Prefix denoting the AID or the entity
assigning the role ID
AM = Access Mode
SC = Security Conditions
CHA = Cert. Holder Authorisation
(Prefix, Role ID)
SM = Secure Messaging

## Slide 18: Hashing

## Slide 19: Certificates
PKCS15 distinguishes - x509Certificates - x509Attribute Certificates - spkiCertificates - pgpCertificates - wtlsCertificates - x9-68Certificates but no cvCertificates!!

## Slide 20: Card Verifiable Certificates
CPI CAR CHR CHA OID PK SIG.CA
- CPI = Certificate Profile Identifier
- CAR = Certification Authority Reference (Authority Key Identifier)
- CHR = Certificate Holder Reference (Subject Key Identifier)
- CHA = Certificate Holder Authorisation (Authority || Role Identifier)
- OID = Object Identifier of PK Algorithm
- PK = Public Key of Certificate Holder
- SIG.CA = Signature of Certificate Issuing CA

## Slide 21
- Template tags for all security services
(e.g. user authentication service, digital signature service,
entity authentication service, key cipherment service)
- DO Instruction set mapping ISM (regular command)
- DO Command to perform (if command is different form that in ISM)
- DO Object Id of the algorithm
- DO Algorithm reference (as used by the card)
- DO Key reference (as used by the card)
- DO Key file id (some cards select the key file containing the key to be used)
- DO Certificate file id (if present then the file contains the certificate )
- DO Certificate reference (used e.g. if the certificate is not stored in the card)
- DO Certificate qualifier (e.g. X.509 certificate, ICC certificate)
- DO PIN usage policy (present if the security service is PIN protected)
Security Service Descriptor

## Slide 22: Security Service Descriptors
Indication of supported algorithms, DSI schemas, hash functions
Indication of user authentication method
Indication where to find certificates
Indication of implementation variants
Support of migration

## Slide 23: SSD construction (1)
- For each security service provided by the card exists one or more SSD templates
- Inside an SSS template is one DO mandatory: the DO „command to perform“ - Use e.g. for VERIFY: - command class is present - PIN reference is present - PIN length is present possibly with padding - presentation form is present: plain value or with SM
- Use e.g. for CHANGE RD: - command class is present - PIN reference is present - usage option is present, e.g. old PIN required/not required in the command - PIN length is present possibly with padding - presentation form is present: plain value or with SM

## Slide 24: SSD construction (2)
- Use e.g. for digital signature function: - the MANAGE SECURITY ENVIRONMENT to perform is presented - the HASH command, if needed, is presented - The PERFORM SECURITY OPERATION command is presented for the digital signature compuation - Different methods for Dig. Sig. Input constructions can be denoted by the DO OID or the DO AlgID E.g. PKCS#1 or ISO 9796-2 rnd
- The FIDs of related certificate files are given

## Slide 25: Working with PKCS#15 (1)
The usage of PKCS#15 requires - selection of DF(PKCS15) - selection of EF(ODF) for getting the pointer information - reading EF(ODF) - selection of EF(AODF) for getting the PIN information - reading EF(AODF) - selection of EF (PrKDF) for getting the signature key information - reading EF(PrKDF) - selection of EF(CDF) for getting the certificate information - reading EF(CDF) - selection of EF(PuKDF) for getting the root CA PuK information - reading EF(PuKDF)

## Slide 26: Working with PKCS#15 (2)
To do this all is not very efficient. Therefor: - Read the information once from the card and store it under a card reference, e.g. the ICC Serial Number ICCSN or - keep the information outside the card and store in the card the card profile identifier pointing to the outside information
Open problem: there is no indication whether the PKCS15 files are - reocrd-oriented or - transparent.

## Slide 27: File Structure of DF.SIG